## Slide 1: Session 1

## Slide 2
This session will cover:
This session will cover:

## Slide 4: Occupational Safety and Health Administration (OSHA)
Robotics
Studies indicate that many robot accidents occur during non-routine operating conditions, such as programming, maintenance, testing, setup, or adjustment. During many of these operations the worker may temporarily be within the robot's working envelope where unintended operations could result in injuries.

## Slide 5: Robotic Safety
SOLDERING
Soldering can be dangerous because of the heat from the iron and the chemical fumes and vapors released from the solder and flux, respectively. When soldering, observe the following points:
Wear eye and face protection.
Solder in well-ventilated areas.
Never touch the iron/gun. It heats to extreme temperatures that will cause severe burns. Wear cotton clothing that covers your arms and legs. Keep your soldering iron in its protective holder when not actually being used.
Always wash your hands with soap and water after handling solder.
Do not leave any hot tools, where someone can accidentally contact the hot element. ALWAYS ASSUME IT’S HOT!!!!

## Slide 6: Robotic Safety
STORED ENERGY
Plan out the required activities when servicing or making repairs to the robot. Make sure all teammates are aware that work is being done on the robot. Address the following:
Ensure no one is working on the robot when it will be energized during repairs.
Electrical Energy: Disconnect the electric power source
Always de-energize the robot before working on it by unplugging batteries. Open the main circuit breaker (“re-set” lever is released).
Pneumatic Energy: Always vent any compressed air to the atmosphere.
Relieve any compressed or stretched springs or tubing and lower all raised components.

## Slide 7: Robotic Safety
BATTERY SAFETY
CAUTION: Batteries contain acid. This substance, H2SO4, is a corrosive, colorless liquid that will burn your eyes, skin, and clothing.
Any battery that is visibly damaged in any way is dangerous and unusable, and should be set aside and handled accordingly.
Care must be taken when recharging batteries. Hydrogen can build up and explode.
First Aid: Neutralize it by pouring the sodium bicarbonate (baking soda) on all wetted surfaces.

## Slide 8: Robotic Safety – First Aid
Injury | First Aid
Cuts - small | Wear gloves Wash – Neosporin - Bandage
Cuts - large | Clean, bandage, apply pressure
Eye Injury - Foreign object or Chemical | Flush with water
Burn - Heat | Wash in cold water – Apply Ice – Apply Aloe
Burn - Chemical | Wash site thoroughly with soap and water
Robot becomes self aware | Have "Fail Safe" shut down switch
You become enslaved by robot | "Obey" then Plan rebellion
*** Call 911 or seek medical attention if injury is serious ***

## Slide 9: Engineering Notebook
An Engineering Notebook is a place to document your ideas and work.
It is a legal document
It can be used for Patents and Legal
Each entry should be dated
It should have references, contacts, drawings, formulas, empirical results, etc.

## Slide 10: Your Engineering Notebook Should Contain
A description of the problem you are solving
Design ideas
List of components
Circuit Diagram
Drawings of your robot
Code listings
Experiments (challenges) and their results
Your observations
Short Summary of the project

## Slide 11: The ParksBot 100 Computational Power to solve all our problems
What is it:
An Arduino Nano
AtMega328
  The high-performance Microchip picoPower 8-bit AVR RISC-based microcontroller combines 32KB ISP flash memory, 2KB SRAM, 23 general purpose I/O lines, 32 general purpose working registers, serial programmable USART, a 6-channel 10-bit A/D converter, The device operates at 5.5 volts @ 16MHz.
What we’ll learn:
Setup our software for programming
Basic Arduino programming
How to write a function
Controlling LEDs

## Slide 12: Software Installation
Arduino IDE
https://www.arduino.cc/en/main/software
CH340 Serial Drivers
Windows CH340 Driver
Macintosh Drivers for CH340 Driver

## Slide 13: Arduino IDE
Test your connection with Blink
Look under File->Examples->Basic->Blink

## Slide 14: Blink Program
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);) delay(1000);
digitalWrite(LED_BUILTIN, LOW); delay(1000);
}

## Slide 15
The ParksBot 100:
Specializes in computational abilities
And will provide the brains of our project
Blinking
Light
The ParksBot thinks a lot, but doesn’t
Move. You might call it a Ramblin Wreck!
What we’ll learn:
Setup our software for programming
Basic Arduino programming
Controlling LEDs
Can you make the ParksBot signal SOS?
Challenge:
Can you make a function that turns on the LED for a given number of ms?
Challenge:

## Slide 16: Session 2

## Slide 17
Our progress

## Slide 19: Fields of Robotics
Human-Robot Interface
Mobility – Movement
Manipulation – interacting with the environment
Programming – robotic control and functionality
Sensors – real world feedback

## Slide 20: Home Work
Find two toothbrushes (can be used)
  Cut off the head of the toothbrush
Pick a field of robotics to discuss with your counselor.
  Find an image that aids in your discussion
Update your engineering note book
Try to add the Right Sonar to the robot.
  Define where the wires go (VCC, GND, Trig, Echo)
  Modify the code to read from both the right and left sonar.

## Slide 21: The SauerBot 200 Using Sonic Technology to Geo-Caching
What is it:
HC-SR04 Sonic Depth Sensor
Uses sound to measure distance to objects
The SauerBot is not powered by Mountain Dew
What we’ll learn:
How a sonic sensor works
How to add library’s for Arduino
How to use a serial monitor
How to use if statments

## Slide 22: The HC SR04 Sonic Sensor

## Slide 23: Using the Sonic Sensor

## Slide 24: Document in your Engineering Journal
Circuit diagrams
Code
Tests

## Slide 25
Bread Board Connectivity
Jumpers plugged into
The board are connected to other jumpers plugged into the same green aligned holes

## Slide 26
Bread Board Connectivity
Jumpers plugged into
The board are connected to other jumpers plugged into the same green aligned holes

## Slide 27
Right Forward
Left Forward
Back
The SauerBot 200 Using Sonic Technology to Geo-Cache
Can you figure out the circuit for adding a sensor on the right?
Challenge:

## Slide 28: Programming the HC SR04
#include <NewPing.h>
const int LEFT_SENSOR_TRIG_PIN=11;
const int LEFT_SENSOR_ECHO_PIN=12;
const int MAX_DISTANCE=200; // max distance in cm
NewPing LeftSonar(LEFT_SENSOR_TRIG_PIN,LEFT_SENSOR_ECHO_PIN,MAX_DISTANCE);
void setup() {
// put your setup code here, to run once:
Serial.begin(115200);
delay(5000);
}
void loop() {
// put your main code here, to run repeatedly:
int LeftDistance=LeftSonar.ping_cm();
Serial.print("Left Ping: ");
Serial.print(LeftDistance);
Serial.println("cm");
delay(1000);
}

## Slide 29: Session 3

## Slide 30
Our progress

## Slide 32: Robotic Competitions
B.E.S.T Robotics Design Contest
Botball Educational Robotics Program
FIRST: Robotics Competition
FIRST: Tech Challenge
National Robotics Challenge
Descriptions of these competitions:
https://blog.collegevine.com/5-robotics-competitions-for-high-schoolers/

## Slide 33
Right Forward
Left Forward
Back
The SauerBot 300 Using Dual Sonic Technology to Geo-Cache
Can you print if the Geo-Cache is on the right or left?
Challenge:

## Slide 34: The crAshley 400 Clears the way for others to follow!
What is it:
A Bristle Bot
2 DC 3V 12000RPM Micro Flat Vibration Motor
Uses vibrating bristles for locomotion
Able to crash into objects easily
What we’ll learn:
Using Pulse Width Modulation to control analog devices
How to trim the toothbrush bristles to promote locomotion
How to create locomotion for a bristle bot
How to tune a bristle bot’s steering
Trim Bristles to form a slant

## Slide 35: Pulse Width Modulation
As its name suggests, pulse width modulation speed control works by driving the motor with a series of “ON-OFF” pulses and varying the duty cycle, the fraction of time that the output voltage is “ON” compared to when it is “OFF”, of the pulses while keeping the frequency constant.
AnalogWrite(177) ~ 3V
255/5v * 3v => 177
177
What width would we program for 3V for our Motor?
78
177
78
177
78
Average 3V
5V On
0V Off

## Slide 36
Right Forward
Left Forward
Back
Basic Motor Circuit Only

## Slide 37
Right Forward
Left Forward
Back
What Our Robot Looks Like with Sensors and a Motor

## Slide 38
Right Forward
Left Forward
Back
What Our Robot Looks Like with Both Sensors and Both Motors

## Slide 39
Right Forward
Left Forward
Back

## Slide 40: Locomotion Code
#define RIGHT_MOTOR_PIN 5
#define LEFT_MOTOR_PIN 6
#define LEFT_VIBRATE 150
#define RIGHT_VIBRATE 150
#define VIBRATE 150
#define NO_VIBRATE 0
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud to see ping results.
pinMode(RIGHT_MOTOR_PIN, OUTPUT);
pinMode(LEFT_MOTOR_PIN, OUTPUT);
delay(5000);
}
void standStill(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("stop");
delay(seconds * 1000);
}
void goForward(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, RIGHT_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, LEFT_VIBRATE);
Serial.println("go forward");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
….
}
void turnLeft(int seconds) {
…..
}
void calibrateMovement() {
goForward(5);
standStill(5);
goForward(5);
standStill(5);
goForward(5);
standStill(5);
goForward(5);
standStill(5);
turnLeft(5);
standStill(5);
turnLeft(5);
standStill(5);
turnRight(5);
standStill(5);
turnRight(5);
while (1) {};
}
void loop() {
calibrateMovement();
}
Can you write the functions for turnRight and turnLeft?
Challenge:
Can you get your crAshley to go straight?
Challenge:

## Slide 41: Session 4

## Slide 43: Robotics Careers
The career choices for robotics are almost endless but here are a few examples
  - Automotive Industry
  - NASA
  - Boston Dynamics
  - Software Engineering
  - Consumer Markets
  - Household robots
  - Prosthetics
  - Military

## Slide 44: Education for a Robotics Career
Electrical Engineering (Sensors, computation)
  Control Systems (Mobility)
Computer Engineering (Programming, computation, human-robot interface)
Robotic Engineering (human-robot interface, system integration)
Computer Science (Programming, AI, ML)
Mechanical Engineering (manipulators, mobility)
Bio-Medical Engineering (medical robots)
https://www.youtube.com/watch?v=zauYACP2lOc
OSU Collaborative Robotics Institute

## Slide 45
Right Forward
Left Forward
Back
What Our Robot Looks Like with Both Sensors and Both Motors

## Slide 46: Toothbrush Locomotion (BristleBot)
HARD brush heads work best
Trim the bristles to be at an angle
Place the brushes in parallel

## Slide 47: Session 5

## Slide 48
Our progress

## Slide 50: Put all the tech of the ParksBot, Sauerbot, and crAshleyBot into one and what do you get? The FischBot 500 Able to navigate the challenges
What is it:
An autonomous robot
Utilizes depth sensors and locomotion to avoid obstacles
What we’ll learn:
Algorithms for Obstacle avoidance
How to debug
Challenges in navigation

## Slide 51: FischBot Navigation
Right
Sensor
Left
Sensor
Forward
Right
Sensor
Left
Sensor
WALL
Stop
if an object isn’t close go forward
if an obstacle is really close to both the right and left sensor stop

## Slide 52: FischBot Navigation
Right
Sensor
Left
Sensor
Right
Sensor
Left
Sensor
WALL
Turn Right
Turn Left
WALL
if an object is close to the right sensor turn left
if an object is close to the left sensor turn right

## Slide 53: What’s a Conditional Statment
In English
IF the distance is less than a mile then I’ll walk
ELSE if the distance is less than five miles then I’ll take a bus
ELSE if the distance is less than 100 miles then I’ll drive a car
ELSE take a plane
Examples in Arduino (C Language):
if (condition) {
Action;
}else if (condition) {
Action;
}else {
Action;
}
Condition
Action
If(distance<1){
Serial.println(“let’s walk”);
}else if (distance<5){
Serial.println(“let’s take a bus”);
}else if (distance<100){
Serial.println(“let’s drive”);
else{
Serial.println(“Let’s fly!!”);
}

## Slide 54: STOP
Right
Sensor
Left
Sensor
Stop
COLLISION_DISTANCE
WALL
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 3cm
const in COLLISION_DISTANCE=3;
If ((RightDistance<COLLISION_DISTANCE) ||
(LeftDistance<COLLISION_DISTANCE)){
StandStill(1);
}
If an object is closer than the COLLISION_DISTANCE in either the right or left side, then stop
Code
3cm
|| symbol represent logical OR

## Slide 55: RIGHT TURN
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
TURNING_DISTANCE is the distance in which the robot needs to begin turning to steer around the object
By experiment this is about 15cm
const int TURNING_DISTANCE=15;
If (RightDistance<TURNING_DISTANCE){
GoLeft(3);
}
If an object is within TURNING_DISTANCE on the right side, then turn left
WALL
Code

## Slide 56: LEFT TURN
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
TURNING_DISTANCE is the distance in which the robot needs to begin turning to steer around the object
By experiment this is about 15cm
If an object is within TURNING_DISTANCE on the left side, then turn right
WALL
If (LeftDistance<TURNING_DISTANCE){
GoRight(3);
}
Code

## Slide 57: FORWARD
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
GoForward(2);
If we aren’t turning left, right, or stopping, then there are no objects. Go forward!!
No objects
Code

## Slide 58: Putting It All Together
Right
Sensor
Left
Sensor
Stop
COLLISION_DISTANCE
TURNING_DISTANCE
}else If (RightDistance<TURNING_DISTANCE){
GoLeft(3);
}
If ((RightDistance<COLLISION_DISTANCE) ||
(LeftDistance<COLLISION_DISTANCE)){
StandStill(1);
}
}else{
GoForward(2);
}
}else If (LeftDistance <TURNING_DISTANCE){
GoRight(3);
}

## Slide 59: Tune and Demonstrate your Robot
Can you get your FischBot to navigate through a series of obstacles?
Challenge:
Can you tune your robot to go straight?
Left?
Right?
Challenge:
Can you write code such that your FischBot tries to travel in the same direction while avoiding obstacles?
How would you do it?
Super Challenge:

## Slide 60: BACKUP

## Slide 61: Uninstalling From Macinstosh
A couple of Mac users have said “the driver crashes my mac Sierra how do I uninstall”.
Firstly regards the crash make sure you installed the 1.3 version of the driver, not the old one. You could download it directly from the Manufacturers Website in case they have issued an update since I wrote this page.
Secondly a quick google search reveals that this is how you uninstall:
Open a terminal and type: cd /Library/Extensions/
Verify that the .kext file is present: ls | grep usbserial.kext
Output should be: usbserial.kext
Then type: sudo rm -R usbserial.kext
Verify that the .kext file has been removed: ls | grep usbserial.kext
Output should be empty.
After you should remove the files stored in receipts folder: cd /private/var/db/receipts/
Find the enties: ls | grep usbserial*
Output should be: codebender.cc.ch34xinstaller.usbserial.pkg.bom codebender.cc.ch34xinstaller.usbserial.pkg.plist
Remove each one of the files of the above list: sudo rm -r filename`

## Slide 62: Locomotion Code
#define RIGHT_MOTOR_PIN 5
#define LEFT_MOTOR_PIN 6
#define LEFT_VIBRATE 150
#define RIGHT_VIBRATE 150
#define VIBRATE 150
#define NO_VIBRATE 0
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud to see ping results.
pinMode(RIGHT_MOTOR_PIN, OUTPUT);
pinMode(LEFT_MOTOR_PIN, OUTPUT);
delay(5000);
}
void standStill(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("stop");
delay(seconds * 1000);
}
void turnLeft(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("turn left");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void goForward(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, RIGHT_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, LEFT_VIBRATE);
Serial.println("go forward");
delay(seconds * 1000);
standStill(0);
}
void calibrateMovement() {
goForward(5);
standStill(5);
turnLeft(5);
standStill(5);
turnRight(5);
standStill(5);
while (1) {};
}
void loop() {
calibrateMovement();
}

## Slide 63: Navigation Code
Setup
const int TURNING_DISTANCE=15; // in centimeters
const int COLLISION_DISTANCE=3; // in centimeters
Loop
void loop() {
int RightDistance = RightSonar.ping_cm();
if(RightDistance==0){
RightDistance=MAX_DISTANCE;
}
int LeftDistance = LeftSonar.ping_cm();
if(LeftDistance==0){
LeftDistance=MAX_DISTANCE;
}
Serial.print("Left Ping: ");
Serial.print(LeftDistance);
Serial.print(" Right Ping: ");
Serial.print(RightDistance);
Serial.println("cm");
if((RightDistance < COLLISION_DISTANCE) ||
(LeftDistance < COLLISION_DISTANCE)){
standStill(1);
}else if (RightDistance < TURNING_DISTANCE){
turnLeft(3);
}else if (LeftDistance < TURNING_DISTANCE){
turnRight(3);
}else{
digitalWrite(LED_BUILTIN, HIGH);
goForward(2);
digitalWrite(LED_BUILTIN, LOW);
}
}

## Slide 64
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
FischBot 500
Troop 605
Robotics Merit Badge
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires